## Slide 1: Security protections across NXP Edge Processing Portfolio
January 2025

## Slide 2: Leverage EdgeLock® security to build protections over device lifecycle
Securely manufacture
Protect integrity and data
Securely connect
Detect, respond,
recover
Encrypted install
of firmware
Encrypted install of keys
Secure debug & config
Remote key install
Measured boot
SW attestation at runtime
Tamper detection
Battery backed monitoring
Device origin attestation
Secure communication
Accelerated networking
Remote key management
Secure boot and initialization
Secure update
TrustZone® SW Isolation
Integrated enclave isolation
Encrypted internal memory
Encrypted external memory
Disk encryption
IP Protection
Cyber Resilience Recovery

## Slide 3
Securely manufacture
Allows OEMs to protect FW confidentiality & SW IP while installed on chip by a third party (contract manufacturer)
Encrypted install of FW
Encrypted install of keys
Allows OEMs to protect secrecy of keys (e.g., FW encryption keys and device access keys and passwords) while installed on chip at manufacturing by EdgeLock 2GO service or by other tools.
Secure debug & config.
Remote key install
Controlled disablement of debugging, programming (such as In System Programming) and testing facilities as well as the securing of debugging interfaces to prevent manipulation of the device state and extraction of sensitive data in field.
Makes use of chip lifecycle management features.
The remote key install allows to seamlessly and securely install various keys and digital (X509) certificates on device, based on NXP cloud platform (NXP EdgeLock 2GO service).
Examples include device origin certificates/keys, FW encryption keys, device access keys, cloud/backend connection keys, application credentials such as Matter Device Attestation Certificates (DAC), WPC Qi charging certificates, etc.
The install can be operated either at silicon distributor, in manufacturing, or over-the-air in field.
EdgeLock 2GO service features overproduction control as well.
1

## Slide 4
Protect integrity
Ensures the integrity, authenticity and version (rollback protection) of SW executed on the MCU/MPU.
Implementation of this function can feature enhancements such as
Support of encrypted boot code & images,
Fast/accelerated mode (for energy saving or fast device start-up)
Quantum safe mode verification based on AES-256 or asymmetric Post Quantum Cryptography (PQC)
Secure boot/initialization
Secure update
On NXP MCUs, secure update authenticates & decrypts a downloaded update image (container) before storing it on FLASH partition in case of dual bank system.
On NXP MPUs, it provides crypto and key management support to OS for SW update verification.
In addition to verification of updates in offline mode and when combined with secure connection function featuring mutual authentication, the secure update function includes the secure distribution of SW to authorized devices only as well as the download of updates from a trusted, authenticated (backend) source only.
TrustZone® SW isolation
Integrated enclave isolation
SW isolation technology at runtime based on alternate execution in time of SW partitions on the same core (with limitation of access to peripherals and memory per partition).
TrustZone® is typically used through Trusted Execution Environment (TEE) SW such as TF-M for MCU or OP-TEE/Trusty for MPUs.
Enhanced isolation of critical & sensitive security functions of the SoC at runtime by hosting these on a dedicated security unit, with its own CPU core, immutable memory (ROM) and other memories, physically isolated from the rest of SoC
Protects SoC integrity and prevents application cores from gaining direct access to sensitive data
Prevents attacks exploiting shared processing/ storage resources typical to some Trusted Execution Environments
NXP offers 2 types of enclaves, depending on MPU/MCU: EdgeLock Secure Enclave (Core Profile) and EdgeLock Secure Enclave (Advanced Profile)
2

## Slide 5
Protect data
(MCU family only)
Provides protection against disclosure and modification of firmware/data at rest on internal, non-volatile memory of MCUs, and herewith mitigates attacks such as FLASH readout for example.
The encryption & decryption are performed on-the-fly (OTF) by dedicated HW engine for optimal performance and seamless cryptographic operations for applications, with a die individual key.
Encrypted internal memory
Encrypted external memory
External memory encryption provides protection against disclosure and modification of sensitive data or firmware stored on external (and therefore accessible) memory, non-volatile or RAM;
This encryption mitigates several types of attacks, such as accessing and probing the memory interface pins on PCB for example. When chip individual key is used, it provides also a binding between the memory and the host processor.
NXP offers cryptographic operations performed on-the-fly (OTF) by dedicated HW engine for optimal performance and seamless cryptographic operations for applications. Some NXP engines provide FLASH decryption only (e.g., OTFAD) some others encryption and decryption on FLASH (e.g., IPED) or RAM (e.g., IEE) .
Beyond decryption of encrypted NV memory content (typically read out of SW or fixed data from FLASH), content can also be authenticated on some NXP processors. This offers an additional layer of protection by mitigating fault attacks or replay attacks but also providing runtime integrity check on executed code (SW authentication when executed in place). This provides a mitigation path against so-called TOC TOU attack (modification of executable between time of check and time of use).
Disk encryption
(MPU family only)
Encryption of user data for protection at rest. On most NXP MPUs, these cryptographic operations are accelerated by cryptographic engines. This function includes the protection of encryption key
3

## Slide 6
Securely connect
Provides evidence of device’s (genuine) identity, origin (e.g. brand) and history (e.g. past owners).
This feature can be optionally enhanced with
Pre-provisioning at/by NXP of device credentials
By built-in Physically Unclonable Function (PuF)
ready-to-use by OEM to prove this identity.
Device origin attestation
Secure communication
Set up of secure communication, authenticated and/or encrypted data, with mutual authentication capability between device and communicating peer, e.g. based on Transport Layer Security (TLS)
Accelerated networking
Provides fast encryption, authentication and/or hashing functionality for fast boot-up, high speed or low latency applications. NXP integrates various acceleration engine (EdgeLock Accelerator) suited for different types of applications (e.g. Time Sensitive Networking, video streaming, etc.)
Remote key management
The key management feature leverages NXP EdgeLock 2GO service to extend the initial secure provisioning of various keys and digital certificates by NXP cloud platform to the management of these credentials in field.
Management includes addition of keys & certificates to install new services on device, to connect to additional cloud platforms,
the renewal of certificates and keys,
the removal of credentials
decommissioning of services and devices
4

## Slide 7
Detect, respond, recover
Provides a remote entity with evidence of loaded software at device boot, and optionally of device configuration parameters (e.g. fuse states, life cycle state)
Measured boot
SW attestation at runtime
Verifies and attests to a remote entity the SW executed on device as well as the device status by providing authenticated measurements of memories performed at runtime by a protected security entity (e.g. EdgeLock Secure Enclave)
Tamper detection
Battery backed monitoring
Monitoring of security events on chip with triggering of protections (such as zeroing of keys) in case of tamper alert.
Also includes monitoring of security events external to the chip (e.g. opening of device case) through tamper pins, either passive (input signal to chip) or active (alteration of a stream of bits sent by the chip)
(MPUs) Security monitor checking various security conditions & detecting security violation and implemented on the always ON domain in lower power section of the System on Chip.
It is typically configurable and includes Real Time clock, monotonic counter and interface for external tamper detection.
On-chip intrusion and tamper detection sensors Include glitch, low/high voltage, clock, temperature and frequency detection.
5
Cyber Resilience Recovery
(MPUs) Protects by hardware a recovery application image allowing to restore the device to a known, trusted, and corruption-free state, in case of anomaly detection, suspicion of attack or attack.
The Cyber Resilience Recovery module also includes the automatic reboot of the chip with the recovery image when associated with an anomaly/attack detection system (local or remote).
It provides key components to meet NIST SP800-193 guidelines for platform firmware resiliency

## Slide 8
Supported Protections | K65 | K81 | MCX A1x | LPC55S6x LPC55S2x | LPC55S1x LPC55S0x | LPC55S3x | MCX N
Encrypted install of FW/keys (manufacturing) | - | √/- | -/- | -/- | -/- | √/√ | √/√
Secure boot/initialization (Enc boot./Fast mode/PQ-secure mode) | - | - | ■ OEM bootloader locked in FLASH | √(√/-/-) | √(√/-/-) | √(√/√/√ [S]1) | √(√/√/√ [S]1)
Secure update3 | - | √ | ■ OEM update FW locked in FLASH | √ | √ | √ | √
Secure debug & configuration | √ | √ | √ | √ | √ | √ | √
Device origin attestation | √ | √ | - | √ | √ | √ | √
Enhanced support Device origin/Identity (Factory programmed unique keys –FPUK- or PUF) | - | - | - | PUF | PUF | PUF | PUF
Remote Key Install/Management (EdgeLock 2GO) | - | - | - | - | - | - | ■ 7
Measured boot2 | - | - | - | √ (DICE) | 1x only (DICE) | √ (DICE) | √ (DICE)
SW Attestation at runtime | N/A | N/A | - | ■ (6x only, TEE) | ■ (TEE) | ■ (TEE) | ■ (TEE)
Phys. tamper detection4 | √ | √ | √ | - | - | √ | √
Device authentication & secure comm. | √ | √ | - | √ | √ | √ | √
Accelerated connections & networking | √ | √ | - | √ (CASPER, HASH-CRYPT) | √ (CASPER, HASH-CRYPT) | √ (ELE-CP5, PKC) | √ (ELE-CP5, PKC)
Encrypted Internal memory on-the-fly | - | - | - | √ | √ | √ | √
Encrypted external memory3 : on-the-fly Flash dec./Flash enc./Flash Auth/RAM enc & dec) | N/A | √/-/-/- | - | N/A | N/A | √/√/√/- | √/√/√/-
TrustZone® Isolation (TEE: TF-M) | N/A | N/A | - | √ (6x only) | ■ | ■ | √
Integrated enclave isolation | - | - | - | - | - | √ (ELE-CP5) | √ (ELE-CP5)
Assurance Level: SESIP /PSA Certified Level | - | - | - | Level 1 (6x) | Level 1 (0x) Level 2 (1x) | Level 3 | Level 3
Additional evidences of conformance | - | - | - | - | - | - | IEC 62443
[S] stands for symmetric crypto 2. If not available, can be added at secondary boot loader level 3. If not available, can be added at application level 4. Sensor and/or tamper pins
5. ELE-CP: EdgeLock Secure Enclave (Core Profile) 6. ELE-AP: EdgeLock Secure Enclave (Advanced Profile) 7. Coming soon
- Not available ■ HW ready √ Available

## Slide 9
Supported Protections | MCX W71 | K32W148 | RW612
Encrypted install of FW/keys (manufacturing) | ■/■ | ■/■ | √/√
Secure boot/initialization (Enc boot./Fast mode/PQ-secure mode) | √(√/√/-) | √(√/√/-) | √(√/-/-)
Secure update3 | √ | √ | √
Secure debug & configuration | √ | √ | √
Device origin attestation | √ | √ | √
Enhanced support Device origin/Identity (Factory programmed unique keys –FPUK- or PUF) | FPUK | FPUK | PUF
Remote Key Install/Management (EdgeLock 2GO) | ■ 7 | ■ 7 | √
Measured boot2 | - | - | √ (DICE)
SW Attestation at runtime | ■ (TEE) | ■ (TEE) | ■ (TEE)
Phys. tamper detection4 | - | - | √
Device authentication & secure communication | √ | √ | √
Accelerated connections & networking | √ (ELE-CP5) | √ (ELE-CP5) | √ (ELE-CP5, PKC)
Encrypted Internal memory on-the-fly | √ | √ | N/A
Encrypted external memory3 : on-the-fly Flash dec./Flash enc./Flash Auth/RAM enc & dec) | N/A | N/A | √/√/√/-
TrustZone® Isolation (TEE: TF-M) | ■ | ■ | √
Integrated enclave isolation | √ (ELE-CP5) | √ (ELE-CP5) | √ (ELE-CP5)
Assurance Level: SESIP /PSA Certified Level | Level 2 | Level 2 | Level 3
Additional evidences of conformance | RED Cyber Trust Mark | RED Cyber Trust Mark | ETSI 303 645 Cyber Trust Mark
[S] stands for symmetric crypto 2. If not available, can be added at secondary boot loader level 3. If not available, can be added at application level 4. Sensor and/or tamper pins
5. ELE-CP: EdgeLock Secure Enclave (Core Profile) 6. ELE-AP: EdgeLock Secure Enclave (Advanced Profile) 7. Coming soon
- Not available ■ HW ready √ Available

## Slide 10
Supported Protections | i.MX RT5xx/RT6xx | i.MX RT1060 | i.MX RT116x/7x | i.MX RT700 | i.MX RT1180
Encrypted install of FW/keys (manufacturing) | √/√ | -/- | -/- | √/√ | √/√
Secure boot/initialization (Enc boot./Fast mode/PQ-secure mode) | √(√/-/-) | √(√/-/-) | √(√/-/-) | √(√/√/√ [S]1) | √(√/-/-)
Secure update3 | √ | √ | √ | √ | √
Secure debug & configuration | √ | √ | √ | √ | √
Device origin attestation | √ | √ | √ | √ | √
Enhanced support Device origin/Identity (Factory programmed unique keys –FPUK- or PUF) | FPUK | - | - | PUF | FPUK
Remote Key Install/Management (EdgeLock 2GO) | - | - | - | ■ | ■ 7
Measured boot2 | √ (DICE) | - | - | √ (DICE) | ■
SW Attestation at runtime | - | - | - | - | ■
Phys. tamper detection | - | - | √ | √ | √
Device authentication & secure communication | √ | √ | √ | √ | √
Accelerated connections & networking | √ (CASPER) | √ (DCP) | √ (CAAM) | √ (ELE-CP5, PKC) | √ (ELE-AP6)
Encrypted Internal memory on-the-fly | N/A | N/A | N/A | N/A | N/A
Encrypted external memory3 : on-the-fly Flash dec./Flash enc./Flash Auth/RAM enc & dec) | √/-/-/- | √/-/-/- | √/-/-/√ | √/√/√/√ | √/-/-/√
TrustZone® Isolation (TEE: TF-M) | ■ | N/A | N/A | ■ | ■
Integrated enclave isolation | - | - | - | √ (ELE-CP) | √ (ELE-AP)
Assurance Level: SESIP /PSA Certified Level | - | Level 1 | - | In certification | In certification
Additional evidences of conformance | - | - | - | In certification | In certification
[S] stands for symmetric crypto 2. If not available, can be added at secondary boot loader level 3. If not available, can be added at application level 4. Sensor and/or tamper pins
5. ELE-CP: EdgeLock Secure Enclave (Core Profile) 6. ELE-AP: EdgeLock Secure Enclave (Advanced Profile) 7. Coming soon
- Not available ■ HW ready √ Available

## Slide 11
Supported Protections | i.MX 6 | i.MX 7S/D | i.MX 7ULP | i.MX 8M | i.MX 8/8X/8XL | i.MX 8ULP
Encrypted install of FW/keys (manufacturing) | √/√ | √/√ | - | √/√ | √/√ | √/√
Secure boot/initialization (Enc boot./Fast mode6/PQ-secure mode) | √(√/-/-) | √(√/-/-) | √(√/-/-) | √(√/-/-) | √(√/8XL only/-) | √(√/-/-)
Secure update (signed/Enc) offline | √/√ | √/√ | √/√ | √/√ | √/√ | √/√
Secure update online with mutual auth. Edge/back-end | OP-TEE | OP-TEE | OP-TEE | OP-TEE | OP-TEE | ELE-AP8
Secure debug & configuration | √ | √ | √ | √ | √ | √
Device origin attestation | √ | √ | √ | √ | √ | √
Enhanced support Device origin/Identity5 | - | - | - | - | - | FPUK
Remote Key Install/Management (EdgeLock 2GO) | - | - | - | - | - | ■ 9
Measured boot | - | - | - | Normal world | Normal world | ■ (ELE-AP8)
SW Attestation at runtime | - | - | - | Normal world | Normal world | ■ (ELE-AP8)
Battery Backed monitoring | √ | √ | √ | √ | √ | √
Phys. tamper detection | √ | √ | √ | √ | √ | √
Device authentication & secure comm. | √ | √ | √ | √ | √ | √
Accelerated connections & networking | √ (CAAM) | √ (CAAM) | √ (CAAM) | √ (CAAM) | √ (CAAM) | √ (CAAM, ELE-AP8)
Disk Encryption with protection of key | √ | √ | √ | √ | √ | √
Encrypted external memory3 : on-the-fly Flash dec./Flash enc./Flash Auth/RAM enc & dec) | √/-/-/- | - | √/-/-/- | - | -/-/-/√(8QM) | √/-/-/-
TrustZone® Isolation (TEE: TF-A/OP-TEE) | √/√ | √/√ | √/√ | √/√ | √/√ | √/√
Integrated enclave isolation | - | - | - | - | - | √ (ELE-AP)
Assurance Level: SESIP /PSA Certified Level | - | - | Level 1 | PSA Certified Level 1 | PSA Certified Level 1 (8QM, 8QXP) | Level 2 (ELE-AP)
Additional evidences of conformance | - | - | - | - | - | -
[S] = symmetric crypto, [H] = Hybrid ECC/PQC 3. If not available, can be added at application level 4. Sensor and/or tamper pins 5. Factory programmed unique keys – KPUK- or PuF
6. (3MB image<50ms) 7. ELE-CP: EdgeLock Secure Enclave (Core Profile) 8. ELE-AP: EdgeLock Secure Enclave (Advanced Profile) 9. Coming soon
- Not available ■ HW ready √ Available

## Slide 12
Supported Protections | i.MX 91/93 | i.MX 94 | i.MX 95
Encrypted install of FW/keys (manufacturing) | √/√ | √/√ | √/√
Secure boot/initialization (Enc boot./Fast mode6/PQ-secure mode) | √(√/93 only/-) | √(√/√/√ [H]1) | √(√/√/√ [H]1)
Secure update (signed/Enc) offline | √/√ | √[H]1/√ | √[H]1/√
Secure update online with mutual auth. Edge/back-end | ELE-AP8 | ELE-AP8 | ELE-AP8
Secure debug & configuration | √ | √ [H]1 | √ [H]1
Device origin attestation | √ | √ | √
Enhanced support Device origin/Identity5 | FPUK | FPUK | FPUK
Remote Key Install/Management (EdgeLock 2GO) | ■ 9 | ■ | ■
Measured boot | ■ (ELE-AP8) | ■ (ELE-AP8) | ■ (ELE-AP8)
SW Attestation at runtime | ■ (ELE-AP8) | ■ (ELE-AP8) | ■ (ELE-AP8)
Battery Backed monitoring | √ | √ | √
Phys. tamper detection | √ | √ | √
Device authentication & secure comm. | √ | √ | √
Accelerated connections & networking | √ (ELE-AP8) | √ (Prime, ELE-AP8) | √ (V2X, ELE-AP8)
Disk Encryption with protection of key | With OP-TEE | √ (Prime) | √ (V2X)
Encrypted external memory3 : on-the-fly Flash dec./Flash enc./Flash Auth/RAM enc & dec) | √/-/-/- | √/√/√/√ | √/√/√/√
TrustZone® Isolation (TEE: TF-A/OP-TEE) | √/√ | √/√ | √/√
Integrated enclave isolation | √ (ELE-AP) | √ (ELE-AP) | √ (ELE-AP)
Cyber Resilience Recovery | - | √ | -
Assurance Level: SESIP /PSA Certified Level | i.MX 93: Level 3 (ELE-AP) | In certification | In certification
Additional evidences of conformance | IEC 62443 Cyber Trust Mark | In certification | In certification
[S] = symmetric crypto, [H] = Hybrid ECC/PQC 3. If not available, can be added at application level 4. Sensor and/or tamper pins 5. Factory programmed unique keys – KPUK- or PuF
6. (3MB image<50ms) 7. ELE-CP: EdgeLock Secure Enclave (Core Profile) 8. ELE-AP: EdgeLock Secure Enclave (Advanced Profile) 9. Coming soon
- Not available ■ HW ready √ Available

## Slide 13: Mitigating various risk profiles with NXP EdgeLock Security
Risk in manufacturing (untrusted location)
Risk on device
(remote exposure)
Risk on device
(physically accessible)
Risk on network (accessible network)
Secure install (encrypted) of SW and keys
EdgeLock 2GO services for install of root of Trust credentials on the device (encryption keys, connection keys, device origin & attestation certificates, FW verification keys, etc.…)
Attestation of origin (OEM)
Attestation of installed SW and configuration
A protection end-to-end
Over device life cycle
Device attestation (origin, network Identity, SW)
Set up of secure connections with support of TRNG and cryptographic services
EdgeLock 2GO services for connection to cloud services and maintenance of credentials in field (removal, revocation, renewal, install)
Bulk data authentication, and encryption if data confidentiality required
Crypto agility
Secure boot
Secure update
Secure connections
Isolation of crypto operations and key storage in Trusted Execution Environment
Enhanced isolation of security functions in EdgeLock Secure Enclave and/or EdgeLock Secure Element
Isolation of sensitive tasks in Trust Execution Environment
Monitoring of device state with runtime device attestation/integrity check
Protections against remote exposure +
Secure debug access
Tamper resistant crypto operations and key storage
Tamper detection on chip or device casing
On-the-fly external Flash decryption & authentication
On–the-fly internal FLASH encryption
Use of EdgeLock Secure Element (or authenticators) for advanced attacks

## Slide 14: NXP EdgeLock Security Protecting the Edge at scale
nxp.com/security
Cyber attacks increases, exposing device manufacturers and infrastructures owners to disruptions, ransomware and many other related costs
A risk & threat analysis is necessary to design and incorporate adequate protections
NXP offers a range of solutions to address different types of attacks, providing resilience, scalability and modularity to match requested protection profile. Furthermore, NXP EdgeLock security facilitates practical deployment of security in field
NXP provides strong support to compliance with EdgeLock assurance program and evidences of conformance to cyber security standards and regulations